## Slide 1: Positive Pressure Ventilation
Characteristics of self inflating bags, flow inflating bags and T-piece resuscitators
When to give PPV
How to position newborn’s head for PPV
How to place a resuscitation mask on newborns face
How to administer PPV and assess effectiveness
How to use ventilation corrective steps
How to administer CPAP
How to place an orogastric tube

## Slide 3: Common terminology for PPV
PIP
  Peak inspiratory pressure: highest pressure administered with each breath
PEEP
  Positive end expiratory pressure: gas pressure maintained in lungs between breaths when baby receiving assisted breaths

## Slide 4: Common terminology for PPV
CPAP
  Continuous positive airway pressure: pressure maintained in lungs between breaths when baby is breathing spontaneously
Rate: # of assisted breaths administered per minute
IT: inspiratory time
  duration of inspiratory phase of each PP breath
Manometer: gauge used to measure gas pressure

## Slide 6: Different types of resuscitation devices used to ventilate newborns: SELF INFLATING BAG
Notes: If not attached to O2 source, it will fill with room air 21% O2. does not require compressed gas or a tight seal to remain inflated. PIP controlled by how hard bag squeezed. PEEP by valve attached to bag. Gas does not flow out of mask unless gag is squeezed, so cannot administer CPAP or free flow O2. Pop off valve, limits peak pressure to 30-40 cm H2O

## Slide 7: Flow Inflating Bags
Notes: Inflates only when compressed gas source is flowing into bag and outlet is sealed, tightly applied to face. Flow control valve adjusts PIP, and controls balance of amount gas flowing into bag and gas escaping . PEEP, CPAP and free flow O2 controlled by balance in gas flow.
Manometer should always be used

## Slide 8: Flow Inflating Bag

## Slide 9: T-piece resuscitator

## Slide 10: Indications for PPV
Apnea (not breathing)
Gasping
Heart rate < 100 beats per minute
O2 saturation
  < the target range despite
  free flow O2 or CPAP

## Slide 11: PPV preparations
Clear secretions from airway (mouth and nose)
Position yourself at baby’s head
Position the baby’s head and neck
Select the correct sized mask
Place the mask on the baby’s face
Select O2 concentration

## Slide 15: Ventilation Rate
40-60 breaths per minute

## Slide 16: O2 Concentration
>35 weeks gestation, set blender to 21% O2
< 35 weeks gestation, set blender to 21-30% O2
Flowmeter to 10 L/minute
Adjust O2 concentration according to
pulse oximeter reading on baby’s
pre ductal saturation

## Slide 17: Pressure used to start PPV
Start PIP at 20-25 cm H2O
  Full term babies may requires 30-40 cm H2O
  Decreases pressure after few breaths
Administer PEEP with initial inflating breaths, 5 cm H2O
Watch gentle rise and fall of chest
Beware of too much Pressure: PNEUMOTHORAX
Notes: Fetal lung fluid within alveoli replaced with air for gas exchange. Pressure moves fluid out of air spaces and inflate the alveoli. Avoid too much pressure

## Slide 18: Evaluate baby’s response after 15 sec of PPV
1- Heart rate is increasing
2- Heart rate is not increasing
  A- Chest IS moving
    Continue PPV, assess HR after another 15 sec
  B- Chest IS NOT moving
    Ventilation corrective steps:
      MR. SOPA
      If chest moves, continue PPV, assess HR after 15 sec

## Slide 19: MR. SOPA
M = Mask adjustment R= Reposition airway Try PPV and reassess chest movement
S= Suction mouth and nose O= Open mouth Try PPV and reassess chest movement
P= Pressure increase Try PPV and reassess chest movement
A= Alternative Airway (endotracheal tube or laryngeal mask)

## Slide 20: Check baby’s heart rate after 30 secs of correct ventilation
HR > 100 bpm
  Continue PPV, monitor chest movement, HR, respiratory effort
  Discontinue PPV when HR continuously > 100 bpm + spontaneous respirations

## Slide 21: Check baby’s heart rate after 30 seconds of correct ventilation
HR> 60 bpm but < 100 bpm
  Is chest moving? Breath sounds equal both lungs?
  Adjust 02 concentrations to Fi02 to 100%
  Consider alternative airway
HR < 60 bpm
  Is chest moving? Breath sounds equal both lungs?
  Adjust O2 concentration to Fi02 to 100%
  Insert alternative airway and provide PPV x 30 secs
  Chest Compressions

## Slide 22: Baby breathing spontaneously, HR > 100 bpm, but labored breathing or Low 02 sat with free flowing 02
CPAP
  Not appropriate if baby NOT breathing spontaneously or HR < 100 bpm
  CPAP maintains pressure within lungs of a spontaneously breathing baby, keeps lungs inflated at all times (even end of exhalation)
  Adjust PIP and PEEP
    PEEP: pressure maintained between breaths when a baby is receiving assisted breaths
Notes: Adjust PIP and PEEP before placing mask on baby’s face: hold mask tightly on hand,

## Slide 23: CPAP
  *CPAP during initial stabilization period
    -Tight seal with mask of T-piece resuscitator or flow inflating bag
    -CANNOT USE SELF INFLATING BAG
  *CPAP after initial stabilization period
    -Nasal prongs/mask
    -Bubbling water system, dedicated CPAP device or mechanical ventilator

## Slide 25: Orogastric Tube
During PPV with a mask, or CPAP
Equipment:
  8F feeding tube
  Large syringe 10 ml
  Tape
Notes: Gas enters esophagus and stomach, interferes with respiration

## Slide 26
Notes: Insertion:
  Measure bridge of nose to earlobe and to point halfway between xiphoid process and umbilicus
  Insert through mouth
  Attach syringe, remove gastric contents
  Remove syringe and leave end of tube open, tape tube to cheek
  Continue ventilation

## Slide 27: CO2 Detector
CO2 exhaled from lungs during effective ventilation
Place CO2 detector between mask and PPV device
CO2 detector will turns yellow during each exhalation if effective ventilation
If CO2 detectors stays blue/purple, you are not providing correct ventilation. Need alternative airway

## Slide 28: Self inflating bags
Do not require compressed gas source
Cannot be used to administer free flow O2 thru mask
Cannot be used to administer CPAP to a spontaneously breathing baby

## Slide 29: Flow inflating bags
Require compressed gas source
Must have a tight seal to inflate
Use a flow control valve to regulate the PIP and PEEP
Can be used to administer free flow O2 through the mask
Can be used to administer CPAP to a spontaneously breathing baby

## Slide 30: T-piece resuscitator
Require a compressed gas source
Use adjustable dials to select the PIP and PEEP
Can be used to administer free flow O2 through the mask
Can be used to administer CPAP to a spontaneously breathing baby

## Slide 31: Case Scenario
Become familiar with available PPV equipment
Proceed to case